FLOODING

-Yell “FLOODING”

-LIFEVESTS!

-Determine the source of the WATER

-Is it SALT or FRESH WATER?

If FRESHWATER... RELAX   Tanks are leaking and will not sink the boat.

If SALTWATER ... DO NOT PANIC...ACT FAST...FOCUS.

Check:

#1  Check and CLOSE every through-hull fittings. If gushing water use plugs and hammer tight or RED emergency plug

There are 23 thru-hulls: CLOSE ALL Systematic from BOW to STERN

#2  Other possible areas:

-Engine shaft seal

-Depth and Speed (under floor at entry in MASTER)

-Rudder stock seal

-Engine exhaust

-Hull-to-deck joints

-open hatch

If Vessel has hit something and is HOLED

FIND SOURCE !!!

If hole is larger than 2-4 inches PREPARE to abandon the vessel immediately. Boat will sink in 1-2 minutes. Assemble all crew in cockpit. Start following ABANDON SHIP checklist (EMERGENCY BINDER) until told by captain to cease.

Get AXE, WRECKING BAR, EPOXY, DRILL and SELF-TAPPING SCREWS IN STARBOARD COCKPIT LOCKER MARKED     911

#1 STUFF hole with rags or cushions

#2 Deploy Collision Mat

#3 Use linoleum or plywood coated with underwater epoxy and screw with self-tapping screws to hull

Use ENGINE as auxiliary BILGE PUMP by disconnecting engine raw water intake

- If water quickly reaches top of bunks ABANDON vessel IMMEDIATELY

IT'S JUST A BOAT