Loss of STEERING/RUDDER

-Determine What is Wrong and WHY

RUDDER BINDS UP- HARD TO MOVE

-Check for fishing nets or line. Look aft for anything trailing in water. Put in neutral if engine is running. Try to engage forward and reverse to free prop. If prop is fouled then it is time to get wet. Wet suit, Mask, flashlight and large knife. BE VERY AWARE OF STERN RISING AND FALLING. Always have another person Watching!

THERE IS NO FEELING TO THE WHEEL

-confirm by using other Wheel (if other wheel works then cable has broken on first wheel)

-shaft has broken or blade has detached from shaft

STEERING WITHOUT RUDDER

-Balance Sails. Upwind, trim sails to balance. Downwind, set sails as far forward as possible. Wind speed will dramatically change the balance and heading.

-DEPLOY THE BRIDLE AND WARPS

See drawing on next page.

(Spinnaker Pole is optional)

-LASH spinnaker pole (optional) across aft part of cockpit (OR NO POLE AND JUST THE WINCHES AROUND THE CLEATS) and run long line (with loop in the middle) aft OUTSIDE from port winch through ends of pole to starboard winch. Drag lines from center of bridle. If needed use the Drogue.

Control direction of boat by using winches.

-Other method- use buckets on lines attached to Mid Cleats on each side. Adjust length of lines to change direction of boat.